## Slide 1: Lab 02 Recitation Random Wander, Avoid-Obstacle, Follow-Object
Create a random wander behavior on the mobile robot
Create an obstacle avoidance behavior on the mobile robot
Create an object follow behavior on the mobile robot
Use potential fields to create the collide, avoid, and follow behaviors (shy kid, aggressive kid, curious kid)
Create a smart follow behavior on the mobile robot
Crate a smar twander behavior on the mobile robot

## Slide 2: Avoid-Obstacle Behavior
How does a robot avoid driving into obstacles?
Use a desired heading to a goal while moving away from the obstacle.
goal (xg,yg)
obstacle
robot

## Slide 3: Mobile Robot Disk Abstraction
robot (x, y, f)

## Slide 4: Sum Vectors to Avoid Obstacle
Sum all of the vectors for the distance sensors with respect to the robot reference frame
Steer the robot in the direction of the orientation of the summation vector

## Slide 5: Perception Polar Plot
Notes: Perception Polar Plot
The perception plot is egocentric to eliminate a need for memory representation
Sonar 2 and 3 indicate that there is a wall and no need for memory or reasoning

## Slide 6: Level 0: Avoid Obstacle
Aggressive Kid
Shy
Kid
Notes: Most basic type of control architecture, reactive control is the robot senses and then immediately acts.
This can transition to behavior based control when the behavior is time extended such as wall following or obstacle avoidance.

## Slide 7: Level 0: Follow Object
Curious Kid
Aggressive Kid
Notes: Most basic type of control architecture, reactive control is the robot senses and then immediately acts.
This can transition to behavior based control when the behavior is time extended such as wall following or obstacle avoidance.

## Slide 8: Level 1: Wander
Notes: Level 1: Wander

## Slide 9: Control Schemes
Bang-Bang (On-Off)
Collide Behavior
Controller turns ON when the error is in a given band, stops motor
Controller turns OFF when the error is outside the given band, motors on
Proportional
Run Away or Follow Behavior
Controller is always on but responds proportional to amount of error. The closer the obstacle, the faster the motor moves.
The robot turns proportional to the IR sensors triggered

## Slide 10: Random Wander
GREEN LED

## Slide 11: Demonstration
Collide Behavior
Aggressive Kid
RunAway Behavior
Shy Kid
RED LED
YELLOW LED
RunAway Behavior
Shy Kid
YELLOW LED

## Slide 12: Halt Collide Behavior

## Slide 13: Potential Fields Obstacle Avoidance

## Slide 14: Potential Fields Obstacle Avoidance

## Slide 15: Follow Behavior Curious Kid
GREEN LED
YELLOW LED

## Slide 16: Random Wander & Obstacle Avoidance

## Slide 17: Potential Field Navigation and Proportional Control

## Slide 18: Potential Field Navigation & Proportional Control for Obstacle Avoidance

## Slide 19: Avoid-Obstacle Simulation

## Slide 20: Go-To-Goal & Obstacle Avoidance

## Slide 21: Smart Wander

## Slide 22: Smart Wander

## Slide 23: Smart Following

## Slide 24: Logic Flow Chart
Great way to sketch out how a circuit or code should work
A flow chart is a game plan
The parts of a flow chart are
  Circle
  Diamond
  Square
  Line
Circle is start or stopping point
Square is an action with one outcome
Diamond represents a decision with multiple possible outcomes
Lines connect all of the parts of the flow chart

## Slide 25: Flowchart or Algorithmic State Machine
State – Action
  A rectangular box to denote a state. State name is attached outside the box. Output variable assignments are included in the box
Condition - Decision
  A diamond box to denote a conditional branch.
  One entry and two exits for a binary decision.
Output
  Moore machine outputs based on state input
  Mealy machine generates outputs on state transition
  There is always an entry point. There may be zero to many exit points
Start - End
output
state or
action
condition
Start/
End

## Slide 26: Sample Flow Chart

## Slide 27: Stopwatch Flowchart
Start
Counter=0
Reset=1
Run=0
Button
Counter=Counter+1
Reset=0
Run=1
Clear
Run
1
0
1
Button
Counter=Counter
Reset=0
Run=0
Button
0
0
1
State0
State1
Stop

## Slide 28: State Diagrams
State diagrams can be used to describe the behavior of a system.
The state of a system represents the net effect of all previous inputs to the system
current state
next state
previous state
input
output

## Slide 29: Design Plan: Stopwatch State Diagram
Notes: If I was writing code, I would make functions reset, run and stop

## Slide 30: State Diagrams
state | input | Output | next state
Detect basketball | Ball not found | Ball found | Retrieve basketball
Detect basketball | More balls available | Ball found | Retrieve basketball
Retrieve basketball | Ball found | Ball not retrieved | Retrieve basketball
Retrieve basketball | Ball found | Ball retrieved | Find goal
Find goal | Ball received | Goal not found | Find goal
Find goal | Ball received | Goal found | Shoot basketball
Shoot basketball | Goal found | More balls available | Detect basketball
Shoot basketball | Goal found | Last ball | End
STATE TRANSITION TABLE

## Slide 31: Flowchart (Program Perspective)

## Slide 32: State Diagram (Robot Perspective)
Notes: Creating a state machine in code
Use if-conditions
Use switch cases
Use flags
Use byte with bit switching

## Slide 33: State Transition Table (Robot Perspective)
Robot Boogie Machine |  |  | 
States | Input | Output | Next State
Waiting to Dance | no music hard rock music | country music hip hop music classical music | Line Dance Break Dance Ballet
Break Dance | hip hop music | no music, hard rock music country music classical music | Waiting Line Dance Ballet
Line Dance | country music | no music, hard rock music classical music hip hop music | Waiting Ballet Break Dance
Ballet | classical music | no music, hard rock music hip hop music, country music | Waiting Break Dance Line Dance

## Slide 34: Implementing State Machines
#define RESET 0
#define RUN 1
#define STOP 2
int STATE;
…
void loop() {
if(STATE==RESET) {
if(BUTTON_PRESSED) {
NEXT_STATE = RUN
}
…
} else if(STATE==RUN) {
…
}
STATE = NEXT_STATE;
}

## Slide 35: Switch/Case
switch(STATE) {
case RESET:
if(BUTTON_PRESSED) {
NEXT_STATE = RUN;
}
break;
case RUN:
…
break;
}
STATE = NEXT_STATE;

## Slide 36: Switch/Case
Switch/Case is a different way of implementing an if/else decision
break is important!
  Otherwise, code keeps going on
default is used if none of the cases match

## Slide 37: Pre-Lab 02
Create the pseudocode for the random wander behavior
Create a flowchart for a proportional controller with sensor feedback for avoid obstacle behavior.
Create a flowchart for a proportional controller with sensor feedback for follow object behavior.
Create a state diagram for the smart wander behavior with 3 states including random wander, collide, and avoid obstacle. The inputs that transition the states are no obstacle, danger at obstacle, warning close to obstacle. Make sure to include a state transition table for the smart wander behavior state diagram.
Create a state diagram for the smart follow behavior with 3 states including random wander, collide, and follow object. The inputs that transition the states are no obstacle, danger at obstacle, warning close to obstacle. Make sure to include a state transition table for the smart follow behavior state diagram.

## Slide 38: Lab 02 Demonstration
PART I
Robot random wander
Robot collide
Robot runaway (1,2,3,4 obstacles)
Robot follow (1 obstacle)
PART II
Robot smart wander
Robot smart follow

## Slide 39: Demonstration Requirements
Collide (Aggressive Kid) Alone
Run Away (Shy Kid) Alone
Random Wander Alone
Avoid-Obstacle Behavior (Collide & Run Away)
Follow-Object Behavior (Collide & Follow)
Full State Machine (Smart Follow)
  Random Wander
  Follow-Object Behavior
Full State Machine (Smart Wander)
  Random Wander
  Avoid-Obstacle Behavior
Notes: Your code should be able to turn the states on and off via inputs from a wireless communication device and function calls.

## Slide 40: Submission Guidelines
Demo part I next class
Demo part II one week
Submit memo and code by midnight on Sunday after demo to GradeScope
Comment your code with a proper heading and in-line comments and submit in appendix of Lab worksheet